## Slide 1: An Assessment of Annual Load Estimation Methods in Small Watersheds for Cross Site Comparisons
Nicholas J Gubbins1, Weston M Slaughter2, Michael J. Vlah2, Spencer Rhea2, Emily S Bernhardt2, Matthew RV Ross1
1Colorado State University, Fort Collins, CO; 2Duke University, Durham, North Carolina
Funding and acknowledgments:
This work was funded by NSF Grant #1926420. Thanks to Hubbard Brook Experimental Forest for sensor data.
Works Cited:
Appling et al, 2015, “Reducing bias and quantifying uncertainty in watershed flux estimates: The R package loadflex”
Aulenbach et al, 2016, ‘’Approaches to stream solute load estimation for solutes with varying dynamics from five diverse small watersheds”.
Nava et al, 2019, “An R package for estimating river compound load using different methods”
Solutes are sampled at varying intervals, both within sites as technology advances and between sites as research questions and funding differ. How frequently we sample informs our C:Q knowledge for the solute at the site.
To estimate total load, researchers must fill in gaps using one of a variety of methods. All methods introduce error to load estimation. Selecting the most appropriate method is mostly dependent on the C:Q relationship of the solute and the autocorrelation of samples through time.
Load estimates are improved greatly with high frequency sampling, complete C:Q knowledge, and proper method selection. Solutes with low variability can estimated accurately with sparse data, but dynamic solutes require constant monitoring or effective modeling to accurately estimate.
To assess a load estimate’s quality, we need to assess:
Sampling frequency of underlying data
Hydrologic regime
C:Q relationship
Completeness and stability of C:Q relationship
Annual load is the amount of some solute of interest that moves past a point in a stream. It is calculated from stream discharge and solute concentration data.